## Slide 1: Alternative CC Robotic Systems

## Slide 2
Notes: THE ROBOTICS SYSTEM
There are several approaches to the robotics system. One uses a gantry robot to position the nozzle. Due to large size of the members, potentially high weight, and acceleration / deceleration in motions, a considerable flexing may occur in the gantry system and hence it may be difficult to maintain an accurate position for the nozzle. To remedy this situation, an adaptively controlled platform (light green) with a highly responsive servo system may be attached to the moving platform (purple) of the gantry robot. The nozzle may then be installed on the adaptive platform. The platform is equipped with a laser tracker (red) which accurately senses the platform position using three fixed reference points installed at the site. These reference points could be retro-reflectors (red) installed on fixed poles (three poles in front in the above figure). The arrangement is much like the motion control system for CD and some disk drive heads, were a coarse positioning and an adaptive fine positioning system are used.

## Slide 3
Notes: As the gantry robot platform (purple) makes its inaccurate moves (inaccuracy due to structural flexing), the adaptive platform (light green), which is equipped with a laser range finder or other position detection devices (red), accurately maintains the desired course using the three fixed reference points installed at the construction site. The possible range of the adaptive platform motion in any direction is at least as large as the maximum aggregate flexing and positioning error of the gantry robot platform.

## Slide 5
Notes: At the beginning of the operation where there is no building structure to anchor against, the gantry platform rigidly rests on the ground. The initial (lower) section of the building is constructed by means of elevating the nozzle by its own vertical motion control mechanism. When the mechanism reaches its highest limit the cable lifting system starts to work. By this time the constructed building section can provide stiff support to the suspended gantry frame be means of aforementioned wheeled attachments.

## Slide 6
Notes: To build high-rise structures several cranes that lift the gantry platform by means of cables may be used. Note that the cable lift, which is performed successively after a specified number of layers are constructed, performs coarse positioning in the vertical direction. The nozzle assembly has its own Z motion control for a limited range. This motion control lifts the nozzle layer by layer and in constructing each layer it adaptively compensates for cable positioning inaccuracy.
Also note that the main platform has an extension platform that holds the material (concrete batch, beams, plumbing modules, etc.) and can be accessed by a robotic manipulator that rides on the same main platform.
Material on is periodically replenished by means of elevators or conventional construction cranes .

## Slide 7
Notes: As cables cannot deliver lateral stiffness, the body of the building structure, which is generally very rigid, may be used to anchor the gantry platform. This may be done by means of attachments that have accurate wheels that are tightly in touch with the well cured (several layers below the freshly deposited layers) building external wall surfaces.
An adaptive positioning system may be built into some of the attachments to compensate for small possible dimensional errors such that all wheels around the frame are kept in touch with the building structure.

## Slide 8
Notes: This arrangement requires minimal set up and is practically unlimited as to the height of the structure that it can build.
The support metal tubing sections, which may be visually unappealing on the constructed building, may be cosmetically covered by plastic plugs, or permanently plastered or cemented closed. Leaving them reusable has the advantage of facilitating other automated systems such as painting systems, window washing systems, and robotics emergency rescue systems (which were the subject of serious consideration after the unfortunate WTC event).
The frame lifting approach disclosed here thus has general applications and is not limited to construction by Contour Crafting. The Contour Crafting construction approach, nevertheless, makes the accurate and effortless imbedding of the anchor tube sections possible.

## Slide 9
Notes: In another approach cable cranes are not used to lift the gantry frame, instead the frame climbs the building by means of vertically reciprocating legs (green). Each leg has a pin drive mechanism (orange) that can extend and retract conical headed pins into and out of some metal tubing sections that upon layer wise construction are robotically imbedded into the walls. These pins are accurately spaced by certain number of layers.

## Slide 10
Notes: To build large structures such as apartment buildings, hospitals, schools and government buildings, the overhead gantry platform (yellow) may extend above the width of the structures. Two cranes riding on tracks laid alongside the structure lift the platform. The platform may be equipped with multiple cross members each holding a CC nozzle assembly and a robotic manipulator (for beam installation, plumbing, etc.).
Note that he two side cranes move infrequently and stop at a few positions at which construction takes place. While the side cranes are stopped at a given post (i.e., the gantry platform is held in a given position) all necessary construction under the platform is performed for several layers. The platform is then moved by the side cranes to the adjacent post and the construction is resumed. This cycle is repeated until completion.
Conceivably, for very large structures multiple crane/gantry platform assemblies may be used concurrently.

## Slide 11: Dynamic System Control
Material Flow
Computation
Flow Control
Law
Position Sensors
Nozzle Actuator
Nozzle Control
Law
Robot Wheel
Motors
Flow Sensor
Position Sensor
Gantry
Dynamic
Model
Material Flow
Dynamics
System
Dynamics
Desired
Material
Flow
Nozzle
Position &
Orientation
Gantry
Position
Wheel
Torques
Nozzle
Forces
Commanded
Position
Material
Flow
+
-
+
-
Gantry Motion
Controller

## Slide 12
Notes: Another approach to implementation of the Contour Crafting construction concept is the use of mobile robotics. The Construction Mobile Robot may use a conventional joint structure and be equipped with material tanks and delivery pipes. The end effector of the robot carries a CC nozzle which can reach from ground level all the way to the top of a wall. Because of the imprecision involved in positioning, an adaptive fine positioning platform equipped with a global sensing mechanism (e.g., a laser tracker) may be used for nozzle positioning.
If the mobile robot arm could be made of a rigid structure, position sensing at the end effector may not be necessary. Instead, a position sensor (e.g., using laser tracking) may be mounted on the robot base. In this configuration, the robot does not engage in fabrication while in move. Once it reaches a pre defined post, it anchors itself by extending some solid rods from its bottom. Then it starts the fabrication process from the last point fabricated while at the previous post. This arrangement is very similar to some conventional stationary robotics applications such as welding.

## Slide 13
Notes: In its upright position the robot can reach the top of relatively high walls. The robot may position itself at each of the four corners of a room and each time build the layer section of the wall within its reach.
The robot may return to energy charging and material fill location when needed.

## Slide 14
Notes: The mobile robotics approach has some advantages over the single gantry approach. These include ease of transportation and setup, scalability in terms of the number of robots deployed per project, and possibility of concurrent construction where multiple robots work on various sections of the structure to be constructed.
In building a multi-story structure an elevator may be used to transport the robots to various floors.
Note that the shape of the robots differ in this figure, indicating that they do various jobs (construction, plumbing, tiling, etc.)

## Slide 15: Structure-Riding robot
Notes: This figure shows the robot constructing a straight wall. The direction of the motion is toward left.
Note that the details of the Contour Crafting nozzle which has movable trowels are not shown. The CC nozzle can rotate (under on-board computer control) with respect to the vertical axis of the feeding tube.
Also note that much like in other robotics approaches for CC, multiple materials (e.g., for outside surfaces and for core) may be used in this implementation.

## Slide 16
Notes: The material container and the feeding tube which is attached to it can rotate 360 degrees. This allows for creation of various structure shapes such as corners.
Concurrent control of the wheel system, rotation of the material container and transfer tube, and the CC nozzle orientation may be used to create various geometrical features.

## Slide 17
Notes: The wheel platform can swivel so that the robot can climb each completed layer.
The climbing action combined with a 180 degree rotation of the material container (and nozzle system) can also accomplish the construction of wall ends (the robot builds as much of the wall layer as possible and when it gets too close to the end it rotates the nozzle assembly 180 degrees, and then moves backward to climb the layer just build – waiting enough for material to cure before climbing).